## Slide 1
DESSIN
Presentation 16.03.2016 – Hoffselva demo in Oslo, Norway
H. Helness, S. Damman and P. Zinke, SINTEF & Cheng Sun, Inrigo AS
The research leading to these results has received funding from the European Union Seventh Framework Programme (FP7/2007-2013) under grant agreement no. 619039

## Slide 2
WP32 Hoffselva demo site (Oslo, Norway)
Catchment area: 1 427 ha
Number of people connected to the sewer system: 25 500
There are 22 CSO’s discharging into the river
Aprox. 14 km sewer system

## Slide 3
TYPICAL COMBINED SEWER SYSTEM (G. Weiss 2014)

## Slide 4
Monitoring water quality in Hoffselva
and evaluation of solutions

## Slide 5
UFT demonstration plant for lamella sedimentation at Emscher in Germany
Planned installation at Hoffselva in June 2016
T32.1 LAMELLA SEPARATORS FOR IMPROVED SEDIMENTATION

## Slide 6
T32.2 HIGH RATE FILTRATION
HRF benefits:
BOD removal rate 60%
SS removal rate 70%
No need for pretreatment
No chemical needed
Space efficient
Low operational cost
Easy operation and maintenance
www.inrigowater.no

## Slide 7
T32.3 Enable integration of local CSO treatment by innovative monitoring and data communication
On-line sensors
  Flow rate x 2
  Pressure x 2
  Turbidity x 2
  Level x 4
Data acquisition manager (DAQ Manager)
PC with wireless internet
Remote access to desktop

## Slide 8
WP32 Demo site preparation
Risk assessment
  Workshop in November 2014
Site levelling, making of pump sump and fundament
  September-November 2014
Arrival of HRF unit
  February 2015
Public meeting in a nearby sport centre
  March 2015

## Slide 9: T32.4 Demonstration plan
No | Activity | Type of demonstration | Analysis | Coordinated activity
1 | HRF (in progress) Lamella settler (planned from August 2016) | Demonstration during rain events. Activate local water samplers and collect a pre-defined number of samples (on signal, time or flow proportional) Controlled experiments with personnel on-site. (Test conditions depends on actual conditions on-site, but may include various flow rates, water qualities , prolonged run without backwash …) | SS, COD, pH, tot-N, tot-P, bacteria Extended analysis from NIVA SS, COD, pH, tot-N, tot-P, bacteria | Yes No
2 | Water quality and flow | Rain events – activate water sampler with signal from container and collect a pre-defined number of samples (time or flow proportional). Continuous high-resolution data logging of turbidity, discharge and water level. | SS, COD, pH, tot-N, tot-P Photos, videos Photos, videos | Yes No
3 | Stakeholder perceptions | Rain events – activate stakeholder group. Surveys, etc. | Photos, videos | Yes No
4 | Data communication and monitoring | Activate water sampler and alert stakeholder group. Demonstration of continuous data logging | Data trends, system uptime | Yes No

## Slide 10: Example of results from CSO event 28th Nov. 2015
6:36 – 9:06 at the HRF
10:38 – 22:36 down stream at HOFF5 near where Hoffselva runs into the Oslo fjord.
No direct link possible – Many CSOs and no discharge from the demo. to Hoffselva
Monitoring and modelling for ESS – Combination of natural science and stakeholders

## Slide 11
DEMO Site Hoffselva – Monitoring 2014/2015
Hoff5
LogA
Measurement and analysis of discharge and turbidity data, Autumn 2014 and Autumn 2015
CSO-spill upstream from Holmendammen

## Slide 12
DEMO Site Hoffselva – Modelling
Master thesis at NTNU Trondheim, Mads Arntsen, Institute for Hydraulic and Environmental Engineering:
«Monitoring and modelling of water flow and quality at the Hoffselva DEMO site (Oslo)”
January – June 2016
Adaption and application of the existing MIKE URBAN model for Hoffselva (Oslo VAV), in order to simulate the discharges from CSO and surface runoff into the river
1D hydrodynamic modelling of flow and some water quality parameters for selected rain events using HECRAS
Model-based scenario investigations to assess the effect of CSO-treatment solutions on water quality in Hoffselva (“with / without CSO treatment”)
Comparison and discussion of the obtained results with regard to the improvement of water quality in Hoffselva
MIKE URBAN model of Oslo VAV

## Slide 13: Involving "Friends of Hoffselva"
ESS improvements in this case is much about use and non-use value
Will the level of water quality improvement 'make a difference' for the users of the area?
User observation study – combine biochemical testing with observed, 'lived' water quality at CSO overflows
What value will the improvements have for users/residents of the area?
How important? Worth the cost of implementation, in their eyes?
Demand assessment (stated preference, survey) starting later in 2016
One of several 'river forums' in Oslo, about 120 members, resourceful enthusiasts

## Slide 14: Observation study
01.03-01.12 2016
7 observation points along the river
'Normal' conditions and SMS at CSO events
Log form & 3 photos, measure water depth
'Lived experience' – 9 aspects
  Time/weather
  Amount, flow of water
  Appearance of water (colour, turbidity, natural & human-made material)
  Condition of river banks
  Smell
  No. of people in area
  Own activity (leisure, way to work, shopping, etc.)
  Total impression, experience of being by the river (positive-negative)

## Slide 15: Observations 1. March
5 graded response alternatives
Individual variations, but general trends:
  A little less water than usual for the season
  No colour, except some furthest downstream
  Mostly low turbidity
  No smell, except some furthest downstream
  Limited amounts of floating material (natural and human-made)
  Trash at some points, mostly not
  Few people, mostly less than 5 (5-10 at Smestaddammen) (Cold afternoon!)
  Total experience most positive at major dams, less positive furthest down
  'Baseline' established!

## Slide 16: ESS evaluation at Hoffselva
From the Hoffselva study (T32.4)
  Data from tests
    Performance of the solutions
    Water quality in Hoffselva
  Monitoring and modelling
    Water quality in Hoffselva
    Predicted CSO discharge and the effects on water quality in Hoffselva
  Data from observations and stated preference study
    Users perspective and preferences
Combined to give ESS evaluation in Hoffselva by means of the cookbook
  Bullet points above relate to PART IV Impact assessment, but refinement still needed.
  PART I – III partly done, but needs review.

## Slide 17
High Rate Filtration (HRF) Demonstration plant for CSO Control in Hoffselva, Oslo
16.03.2015, Nieuwegein, Netherlands
Inrigo AS LIV-bygget N-7125 Vanvikan Norway
http://www.inrigo.no

## Slide 18: Mechanism of High Rate Filtration (HRF)
Backwash waste
Filtration
Filtered water
Distribution channel
Backwash
Upper screen
No coagulant ！
Filter media
Debris
Upper screen
Raw
wastewater
Raw
wastewater
No bottom screen！
Inlet Water level detection

## Slide 19
Advantages of HRF
Low maintainance, less inspection, no chemicals
Low invest cost, much lower than new piping system
Low energy comsumption, i.e no feed pumps
Low space, less civil engineering work

## Slide 20
HRF demostration plant in Hoffselva

## Slide 22
Demonstration test result
HRF plant on standby for CSO since Sep. 2015
6 times CSO events has been treated and recorded
Water parameters evaluated: COD, BOD, SS, Turbidity, Bacteria
Backwash frequence and cleaning strategy have been investegated
CSO events:
17, Sep., 2015
11, Oct., 2015
17, Nov., 2015
28, Nov., 2015
04, Dec., 2015
08, Feb., 2016

## Slide 23
Overall removal: COD, SS

## Slide 24
CSO event study (07.11.2015)

## Slide 25
COD removal
SS removal

## Slide 26
Nutrition removal

## Slide 27
CSO event study (28.11.2015)

## Slide 28
Metals removal

## Slide 29
03.2016 – 06.2016 Standby test
07.2016 – 10.2016 Comparing test
11.2016 – 06.2017 ESS modelling test
Demostration plan

## Slide 30
Herman Helness
Peggy Zinke
Bård Myhre
Stig Petersen
Sigrid Damman
Rita Ugarelli
Edvard Sivertsen
Cheng Sun
Per Kølner
Frode Hult
Arnhild Krogh
until Sept. 2015
Team Hoffselva
SME's
Research
Site owner